## Slide 1
AUTONOMOUS DRONE UTILITY INSPECTION
UW-TIG: Uncertainty-Weighted Temporal Information Gain for Closed-Loop Defect Inspection
PSG College of Technology · Department of Computer Science and Engineering, Coimbatore
Under the guidance of
Ms. L. Karthika
Guide
Dr. N. Gopika Rani
Co-Guide
Team members
Akhil Ramalingam
23Z207
Anbuchandiran K
23Z209
Neelesh Padmanabh
23Z241
Saumiyaa Sri V L
23Z261
Sowndarya Elangi S
23Z269
Therdhana J P
23Z273

## Slide 2: Problem Statement
2
Utility infrastructure -- buildings, pipelines, towers -- needs repeated inspection for cracks, corrosion and leakage. Today's drone inspection is largely open-loop:
Fixed routes
The drone follows a pre-planned path; what it detects never changes where it flies next.
No memory
Every flight starts from scratch -- a defect seen last month is not tracked or compared.
Uncertainty ignored
A low-confidence detection is treated like a confident one; nothing triggers a second look.
Single-session planners
Recent planners (Rückin 2023, GATSBI 2023/24, Moon 2026) work within one session; none tracks a defect across missions.
Objective
Build a closed-loop drone that detects defects with a trained model, measures its own uncertainty, remembers defects across missions, and decides where to fly next -- and show it beats published planners on the same testbed.

## Slide 3: Abstract
3
This project builds a simulated autonomous drone (PyBullet, gym-pybullet-drones) that inspects an open-air utility yard for surface defects. A YOLOv8 detector trained on 14,471 real UAV photographs (MBDD2025) finds cracks, leakage, abscission, corrosion and bulging, and a test-time-augmentation ensemble estimates each detection's uncertainty. Detections are ray-cast to 3-D positions and stored in a persistent memory (PostgreSQL + pgvector, Neo4j) that tracks each defect across missions. The proposed planner, UW-TIG, builds on recent uncertainty-driven informative path planning (Rückin et al. 2023, Moon et al. 2026) and adds a coverage guarantee, detection uncertainty, defect growth, revisit staleness and a two-step lookahead. It is compared on held-out test seeds against random search and five re-implemented published planners.
0.949
Precision
0.967
Recall
0.953
F1 score
39%
less flight than the best published planner at equal F1
Closed-loop results, mean over 3 scenarios x 5 test seeds x 3 missions

## Slide 4: Literature Survey (2023 - 2026)
4
Paper, authors & year | Technique | Advantages | Limitations
Dhami et al. (GATSBI), ICUAS 2023 Targeted bridge inspection | GTSP routing over target surfaces; detector added 2024 | Cost-aware and inspection-specific | One session; no uncertainty, no memory
Rückin et al., IEEE T-RO 2023 Informative path planning | Model uncertainty (MC-Dropout) drives the path | Real learned uncertainty in planning | One session; goal is retraining the model
Vashisth et al., IEEE RA-L 2024 Adaptive IPP with deep RL | Reinforcement learning on dynamic graphs | Learns to balance exploring and targets | Needs training; no defect history
Petit & Lussier Desbiens (MOAR), ICRA 2024 Risk-aware inspection planning | Multi-objective, risk-aware path planning | Adapts to weather, battery and safety | No perception or defect awareness
Svystun et al., 2024 Wind-turbine UAV inspection | Segmentation-guided trajectory adaptation | 78% shorter inspection time | One structure type; no revisits
Jin et al., 2025 Adaptive surface inspection | Global coverage + local reactive replanning | Handles obstacles missing from the map | Coverage only; no defect detection
Moon et al. (IA-TIGRIS), IEEE T-RO 2026 Incremental informative planning | Sampling-based planner that reuses past plans | Fast online replanning | Generic information gain; no defects
Li et al., RSS 2026 Motion-uncertainty-aware NBV | View selection under motion and measurement uncertainty | Plans over uncertain futures | Reconstruction task, not defect inspection

## Slide 5: Inferences & Proposed Novelty
5
Inferences from the survey
Recent planners (2023-2026) add risk, learning and adaptivity, but plan for coverage or information gain -- none plan around detected defects.
Uncertainty-driven planning (Rückin 2023, Li 2026) uses model or motion uncertainty within a single session.
No reviewed work re-inspects the same defect across missions; 2025 reviews (Nikkhah et al.; Vivaldini, Pěnička & Saska) still list perception-driven flight planning as open.
Recent YOLO detectors report 0.91-0.98 precision, mostly on single-class or private data.
UW-TIG: what is new
Coverage guarantee -- every wall is seen once before anything else; fixes the recall ceiling of cost-normalised greedy planners.
Detector uncertainty -- unsure detections earn a second look (TTA ensemble of a trained YOLO model).
Cross-mission memory -- Postgres + Neo4j track each defect's identity and growth over missions.
Staleness -- areas not seen for a while gain priority (after Alamdari et al.).
Two-step lookahead -- plans one move ahead instead of pure greedy (after Bircher et al.).

## Slide 6: Novelty in Detail: How UW-TIG Decides Where to Fly
6
Score of a viewpoint v: 1.0·InfoGain(v) + 1.5·Uncertainty(v) + 2.0·Growth(v) + 1.0·Staleness(v) − 0.4·Cost(v) (54 views re-scored after every move)
Component | How it works | Why it is needed | Measured effect
1. Coverage guarantee | While any wall is still unseen this mission, choose only among unseen walls' views, scored by InfoGain − 0.4·Cost; full score takes over once all 9 walls are seen. | A plain information-gain score never pays to fly to the far building -- it stopped at 4 of 9 walls on every seed. | Recall 0.556 → 0.967; F1 0.680 → 0.953. The decisive addition.
2. Detector uncertainty | Each frame is run 5 times (original + 4 brightness / noise / blur variants); the spread of confidence is the uncertainty, faded as a spot is viewed more. | An unsure detection should earn a second look instead of being trusted or dropped. | Real but small next to the other terms: shifts the route by under 1 m, no metric changes.
3. Cross-mission memory & growth | Each detection is ray-cast to 3-D and matched to a known defect (Postgres + pgvector); Neo4j keeps its history. Growth = size now − size last time. | A drone that forgets is re-learning every flight; worsening defects need tracking. | Looks count across missions: a defect is reported after 3 looks or one at confidence ≥ 0.45. Growth is ~0 here (test scenarios don't grow).
4. Staleness | Priority rises with time since a spot was last seen: 1 − e^(−0.15 · steps since last view). Adapted from Alamdari et al. | Keeps the drone from fixating on one wall while others go unchecked. | Removing it: F1 0.958, 36% less flight -- currently adds flying, not accuracy.
5. Two-step lookahead | Each view is scored with the best follow-up view after it (weight 0.5); only the first step is flown, then it replans. Adapted from Bircher et al. | Pure greedy choice can walk into dead ends. | Removing it: F1 0.958, 32% less flight -- an open tuning question.
Setting all new weights to zero and switching off the coverage phase and lookahead gives back a plain cost-normalised information-gain planner exactly -- so every gain is measured against it, not against a different algorithm.

## Slide 7: System Architecture
7
Planner
UW-TIG utility
Scores 54 candidate viewpoints and picks the next one
Flight + Camera
PyBullet drone
Flies there (PID physics in demo, kinematic in sweeps) and captures a frame
Detector
YOLOv8 + TTA
Finds defects; 5-view TTA gives confidence and uncertainty
Geometry
Ray-cast to 3-D
Projects each box onto the wall plane to get a 3-D position
Memory
Postgres + Neo4j
Matches defects across missions and records growth
feedback: updated coverage, uncertainty and growth drive the next choice -- and the next mission
Test environment
Open-air utility yard: two equipment buildings plus inspection panels on a pipe rack and a lattice tower -- 9 inspectable surfaces, 54 candidate viewpoints at 1.3 m and 2.2 m standoff. Four scenarios (static, uncertain, multi-defect, growing) with real MBDD2025 photos applied as wall textures.

## Slide 8: Requirements, Dataset & Preprocessing
8
Software requirements
Python 3.12
PyBullet + gym-pybullet-drones (simulation, PID flight)
Ultralytics YOLOv8 / YOLO11, OpenCV, NumPy
PostgreSQL + pgvector (detection log, identity matching)
Neo4j (defect graph across missions)
Docker Compose (runs both databases)
NVIDIA L4 GPU on a rented 32-vCPU machine (training and the 31-wall sweeps)
Datasets
MBDD2025: 14,471 UAV photos, 5 classes; detector training/test and the simulator's wall textures (1,448 held-out test images).
dacl10k: real bridge-inspection photos (CC-BY-4.0); 5,362 train images added, 810 held out as a cross-dataset test.
Roboflow corrosion: 851 corrosion/crack images added to training.
Concrete-crack crops: 800 held-out images for an image-level check (never trained on).
SDNET2018: planned, but its download is bot-blocked; replaced by the sets above.
Preprocessing
Aspect-correct crop: photos cropped to each wall's true shape at 1536 px (was stretched ~2.2x).
Square pixels: 320x240 camera frames resampled before detection.
Oversampling: bulge images repeated ~4x in training.
TTA ensemble: 4 photometric variants per frame give an uncertainty score.
On-wall check: hits outside the wall rejected -- removed 51-75% of false positives.

## Slide 9: Detection Model & Evaluation
9
Model: YOLOv8s · 640 px · 100 epochs on an NVIDIA L4 · bulge oversampled ~4x · uncertainty = spread of confidence across TTA views
Our detector -- held-out test set (1,448 images)
Class | Precision | Recall | F1
Crack | 0.84 | 0.75 | 0.79
Leakage | 0.90 | 0.92 | 0.91
Abscission | 0.87 | 0.78 | 0.82
Corrosion | 0.83 | 0.79 | 0.81
Bulge | 0.95 | 0.96 | 0.95
Mean | 0.87 | 0.84 | 0.86
mAP50 0.884 · mAP50-95 0.506
Recent detectors (2023 - 2026)
Paper | Task / data | P | R | mAP50
Ours (YOLOv8s) | 5 classes, public MBDD2025 | 0.874 | 0.842 | 0.884
Huang et al. 2025 (YOLOv11) | Concrete crack, 1 class | 0.913 | 0.766 | 0.864
Li, Shi & Sun 2026 (YOLOv11) | Utility tunnel, private data | 0.932 | 0.924 | 0.926
Inam et al. 2023 (YOLOv5m) | Bridge crack, 1 class | 0.977 | 0.967 | 0.993
Also reviewed: TinyDef-DETR (Shen et al. 2025, transformer, power-line defects) and a saliency-guided YOLOX bridge detector (Hebbache et al. 2025) -- neither reports a comparable number. Higher scores above come from single-class or private datasets; ours is 5-class on public data.
Extra datasets: fine-tuning on MBDD + dacl10k + Roboflow lifted held-out dacl10k mAP50 from 0.004 to 0.184, left MBDD unchanged (0.884 vs 0.886), and did not improve the closed loop -- so the original detector stays the default. Calibration: expected calibration error 0.29-0.33; uncertainty is used only to rank views, never as a probability.

## Slide 10: UW-TIG Planner & Closed-Loop Results
10
Utility(v) = 1.0·InfoGain + 1.5·Uncertainty + 2.0·Growth + 1.0·Staleness − 0.4·Cost (coverage phase first; 2-step lookahead)
Planner | Precision | Recall | F1 | Flight (m) | Coverage
Random baseline | 0.921 | 0.837 | 0.873 | 395 | 1.00
Isler-NBV (classical, 2016) | 0.890 | 0.556 | 0.671 | 31 | 0.44
Bircher et al. 2016 | 0.917 | 0.756 | 0.814 | 48 | 0.67
Dhami et al. (GATSBI) | 0.887 | 0.922 | 0.900 | 125 | 1.00
Alamdari et al. 2014 | 0.924 | 0.967 | 0.941 | 168 | 1.00
Rückin et al. 2023 | 0.959 | 0.944 | 0.950 | 204 | 1.00
UW-TIG (ours) | 0.949 | 0.967 | 0.953 | 125 | 1.00
What the results show
Ties the best published planner on F1 (0.953 vs 0.950) while flying 39% less.
Coverage phase is decisive: F1 0.680 without it.
Removing uncertainty or growth changes no metric: the coverage phase ignores both, and these scenarios have no real growth.
Rückin et al. has slightly higher precision (0.959).
Mean over static, uncertain and multi-defect scenarios x 5 test seeds x 3 missions; each published planner's selection rule re-implemented on the same testbed.

## Slide 11: Scale-up: 31-Wall Yard & Statistics
11
Yard enlarged from 9 to 31 walls (186 viewpoints, budget 50). Same test seeds 0-4, 3 scored scenarios; F1 interval = 95% bootstrap over seeds.
Planner | F1 (31 walls) | 95% CI | Flight (m) | Coverage | F1 (9 walls)
UW-TIG (ours) | 0.921 | 0.906-0.938 | 480 | 1.00 | 0.953
Alamdari 2014 | 0.928 | 0.912-0.947 | 570 | 1.00 | 0.941
GATSBI | 0.912 | 0.894-0.927 | 471 | 1.00 | 0.900
Rückin 2023 | 0.903 | 0.881-0.925 | 860 | 1.00 | 0.950
Random | 0.801 | 0.772-0.836 | 2396 | 0.99 | 0.873
Bircher 2016 | 0.661 | 0.630-0.688 | 209 | 0.52 | 0.814
Isler-NBV | 0.466 | 0.394-0.519 | 177 | 0.32 | 0.671
Reading the numbers
UW-TIG vs Alamdari: -0.007 (CI -0.020 to 0.007) -- a tie.
vs Rückin: +0.018, interval excludes 0; flies 480 m vs 860 m.
Margins shrink as the yard grows; the coverage phase is still decisive.
Fine-tuned detector did not help the closed loop (UW-TIG F1 0.883 vs 0.921).
Ablations repeat: removing uncertainty or growth changes F1 by <0.005; removing staleness/lookahead shortens the flight with no F1 loss.

## Slide 12: Conclusion & Future Work
12
Conclusion
A working closed loop: detect, assess uncertainty, remember, replan, reinspect.
UW-TIG reaches precision 0.949, recall 0.967, F1 0.953 on held-out test seeds.
Matches the strongest published planners on detection at lower flight cost, in a 9-wall and a 31-wall yard.
Reported honestly: margins shrink at scale, and the fine-tuned detector was not adopted.
Every design choice was fixed on separate development seeds before testing.
Future work
Raise the "uncertain" scenario's precision (0.893) above 0.90.
Re-weight the utility so uncertainty and growth actually influence decisions.
Replace TTA with a calibrated uncertainty (temperature scaling or MC-Dropout).
Add real growth data so the growing-defect scenario can be detected.
Re-implement published planners as full systems, not only their selection rules.